Mission Peak Optics Inc.

46941 Rancho Higuera Road, Fremont, CA  94539 USA

(   TEL: 510-438-0384		(   Fax: 510-438-9795

( E-Mail: warrenlin@missionpeakoptics.com ( Web-Site: www.missionpeakoptics.com

MP100-MB; A Low-Cost 470 mm by 370 mm Glass Plate holder Manual Microscope measurement system

The MP100-MB Thin Film Measurement System comes with a manual microscope designed to fit your large application needs with an extra big stage that can accommodate glass plates with area sizes as large as 470 by 370 mm. It also provides state-of-the-art functions to measure such materials as filled cell gap on LCD, polyimide on ITO, color filter CIE Chromaticity, and Color Filter Thickness. MP100-MB is also able to measure common materials like Oxide, Nitride, Photoresist and Polysilicon Films. The powerful software algorithms can perform single, double, and triple layer thickness calculations. As well as special search and fit routines that quickly converge the algorithm and variables into an accurate thickness measurement. MP100-MB comes with both Reflection and Transmission mode for Anti-Reflection coating and Transmission measurement.

The MP100-MB uses a compact multiple grating spectrometer to achieve a wide spectrum range from UV to NIR. The unique video display design provides the operator with an ergonomic view of the sample area thus eliminating tedious viewing through conventional microscope optics. An USB interface connects directly to a notebook computer and allows for fast transfer of data, and then utilizes the modern computer system to quickly process it.

The MP100-MB software user interface is divided into four quadrants that represent measurement setup parameters, visual spectral display, thickness result bar graph, and a thickness result data table. This fully illustrated interface provides instant data return. The main MPO software is also able to work in conjunction with Microsoft Office™ applications, which allows the operator to save measurement data in MS EXCEL™ spreadsheet format and store it within a MS ACCESS™ database for future recall. This collaboration of software allows you to generate the reports that you need easily and in an organized manner.

Specifications (MP100-MB):

Scanning range:			380 nm to 950 nm, standard

Spectrum resolution:		2 nm

Precision:			0.2 nm

Measuring speed:			2 seconds

Measurement specifications:

|  | 1st Layer | 2nd Layer | 3rd Layer 0 -10,000Å | 4th Layer 0 -10,000Å |
| --- | --- | --- | --- | --- |
| Film Type | Objective Lens | Range | 1σ | Range | 1σ | Range | 1σ | Range | 1σ |
| P1/P2/ITO/Oxide/Gla | 5x | 100 - 3000Å | 3Å | 100 - 3000Å | 3Å | 100 - 1500Å | 3Å | 100 - 1000Å | 3Å |
| Oxide/Si | 5x, 10x | 200 - 3,000Å | 2Å |  |  |  |  |  |  |
|  |  | 3,000,- 50,000Å | 5Å |  |  |  |  |  |  |
|  | 40x | 200 - 3,000Å | 2Å |  |  |  |  |  |  |
|  |  | 3,000 - 20,000Å | 5Å |  |  |  |  |  |  |
| Nitride/Si | 5x, 10x | 150 - 2,000Å | 2Å |  |  |  |  |  |  |
|  |  | 2,000- 20,000Å | 3Å |  |  |  |  |  |  |
|  | 40x | 150 - 2,000Å | 2Å |  |  |  |  |  |  |
|  |  | 2,000,- 10,000Å | 3Å |  |  |  |  |  |  |
| Photoresist/Si | 5x, 10x, 40x | 500 - 20,000Å | 5Å |  |  |  |  |  |  |
| Nitride/Oxide/Si | 5x, 10x | 150 - 20,000Å | 5Å |  |  |  |  |  |  |
| Poly/Oxide/Si | 5x, 10x | 100 - 5,000Å | 5Å |  |  |  |  |  |  |
| Oxide/Poly/Oxide/Si | 5x, 10x | 100 - 10,000Å | 5Å | 0 - 5,000Å | 5Å | 0 - 10,000Å | 5Å |  |  |
| Oxide/Al | 5x, 10x, 40x | 2,000 - 20,000Å | 5Å |  |  |  |  |  |  |
| Photoresist/Cr | 5x, 10x, 40x | 500 - 20,000Å | 5Å |  |  |  |  |  |  |
| Oxide/NiFe | 5x, 10x, 40x | 2,000 - 10,000Å | 5Å |  |  |  |  |  |  |
|  | 5x, 10x | 10,000,- 50,000Å | 20Å |  |  |  |  |  |  |
|  | 5x | 50,000 - 150,000Å | 100Å |  |  |  |  |  |  |
| Photoresist/Glass | 5x, 10x, 40x | 500 - 20,000Å | 10Å |  |  |  |  |  |  |
| More to come… |  |  |  |  |  |  |  |  |  |
| Customized film types are available for your applications. |  |  |  |  |  |  |  |

Measuring spot size: 5x Objective is 50 microns, 10x Objective is 25 microns, 20x is 13 microns, 40x Objective is 7 microns

Viewing options: 2" camcorder screen, and dual microscope eyepiece lenses.

Mission Peak Optics Inc.

## 46941 Rancho Higuera Road, Fremont, CA 94539 USA

### Tel: (510) 438-0384		Fax: (510) 438-9795

Website: www.missionpeakoptics.com	Email: sales@missionpeakoptics.com

# Text boxes

# MP100-ME modified to hold larger Glass Plate, with 75 mm by 50 mm stage travel. Low-Cost MP100-FPD.